Sci 206 – Oct 15 2018
Lecture 10

Electricity

- Bart Housen Effect – Some materials take longer to magnetize or require a stronger magnetic field
- Dropping a magnetic material through a electric coil creates a changing magnetic field which repels the oposing force thus slowing down the magnetic material
- A generator uses this principle by flipping a permanent magnet within a coil, thus generating a opposing magnetic field and generating electrcity
- Alternating current allows voltage to be changed easily through the use of a transforming
- Transformer
- A transformer has a series of coils situated within each other around a metal core.
- When voltage is passed through, the magnetic field of the core will cosistently change	direction which will also cause the coil to produce a changing magnetic field.
- As a property of voltages and magntic field, the number of loops in a coil directly relates to the	output voltage
- Each loop increases the volatage, but since you can not create power, so increasing voltage	decreases current.
- Transformers only work with Alternating current
- AC is perfered because it ensures you loose less current due to resitance in the power line over long distances
- Higher current means transmission cables can not be as long
- Fuse prevents too much current from flowing through a circuit by utilizing a encased wire that will melt and break a circuit in the case of excess current.
- Most houses have circuit breaks, which in concept works similarly to fuses, except they use bimetalic stips. The bimetalic strip is composed of two pieces of metal that heat up at different levels. So, when to much current flows through the bi-metalic strip warms and curls thus breaking the circuit.
- Circuit breakers and fuses are designed to prevent fires and are too slow when trying to protect you
- To protect us from electricution, we have Ground Fault Interrupter as the threshold for breaking the circuit is lower
- In a GFCI , live and neutral wires are passed through a coil. If current in = current out, there is no change in magnetic field. But if current out does not equal current in , there is a change in magnetic field which causes internal electronics to break the circuit
- 5mA is considered the safe amount of current for a human
- The test button in a GFCI causes a resistor to draw 5mA from one of the wires