Sci 206 – Oct 12 2018
Lecture 9

Electricity

- Atoms and Electrons
- Electrons orbit the nucleus
- Some electrons break free of the nucleus and can move freely through the metal.
- A conductor is a material that allows for the free movement of electrons
- An insulator is a meterial that does not allow for the free movement of electrons
- You can also force a material that isn’t conductive to be conductive through sheer force
- Defects in a material on an atomic level contributes to a materials resistance.
- Current moves from postive terminals to the negative terminals, but in practice electrons travel from the negative terminal to the postive terminal
- Voltage is proportional to the difference in energy
- Electric circuits resistance
- If you have constant voltage : small resistance gives big current and large amounts of	resistance yields small current
- Ohms Law : V = I R (Voltage = Current * Resistance)
- Voltage is the energy of each charge and current is the number of charges

- Power
- Power is enegry released per time
- Big power yields alot of energy per second
- Small power yields little energy per second
- Power = V I (Voltage x Current)
- Given V = IR and P = I R I , we can conclude that P = I^2 R
- Units of power are watts (W), 1 watt is 1 volt times 1 amp
- In series, charges must power multiple devices on a circult. Additionally, the resistance of each devices adds up and increases the overal resistance of the circuit
- In parallel, a equal amount of charges are provided to each devices, and restiance of other devices does not impact that the performance of other devices.
- In parallel the power source must output more charges to keep up the desired voltage
- Electric charge requires low resistance and free electrons
- Lower tempreatures cause overall resistance to be lower, thus allowing more charges to be passed as atoms are vibrating less
- Free electrons are also required for electric charge to flow, certain materials such as semi-conductors have less free electrons at lower tempratures. Thus, at lower temperatures can also yield higher resistance
- Since electrical wires are not perfect, they also have resistance. As a result, more current, yields less power as more electricty is lost due to the resistance
- Direct / Alternate Current
- Current Direction and voltage difference is constant for direct current
- Current Direction changes for alternating current. Additionally, voltage difference varies.
- Magnets and electrcity
- Electric current makes a magnetic field
- Strength of a field depends on current and nmber of windings.
- Iron bar has magnectic domains that are normaly randomly oriented when there is no externa field
- Domains oriented with the magentic field from the coil grow (others shrink)
- This amplifies the total magnetic strength of the electromagnet
- When a magent comes into a contact with a magnetic element, the magnetic fields from the magent orients the domains in the magnetic element thus causing the magnetic element to become magnetic
- In a permanent magnet, domains are permanently oriented and it requires alot of effort and energy to undo these magnetic domains
- Each loop in a coil connected to a charged source creates a magentic field
- Alternating current
- To make alternating current you need a permanent magent and a coil.
- A change in magentic field caused by moving a magnet inside a coil generates current
- Lenz’s Law : Current induced by a changing magnetic field always produces a magentic field	that opposes the change.
- Pushing a magent into a coil causes the coil to attempt to push back. As a result, work must be	done on the magnet to force the magnet through, this work gets converted into electrical energy
-